## Slide 1: Pbot UNO
MANUAL GUIDE
VARIANTS:
PBot UNO
> Line follower
> Maze Solver
> Sumo fight
Wireless controlled:*
> Bluetooth
> UHF/RF module
with PS2 Controlled
> Ethernet
> Wifi
NEW FEATURES:*
> with Ultrasonic sensor
> with EGRA (Robotic Arm)
> Arduino Expansion IO pins
*(Optional)
Included:
- USB Cable Type A to mini B
-
Notes: <number>

## Slide 2: Pbot UNO
DESCRIPTIONS
VARIANTS:
Pbot UNO
> Line follower
> Maze Solver
> Sumo fight
>Optional
- Add wireless
devices
- Add servo
motors
- it is an upgraded version Pbot UNO Atmega328P, that's allows
the users to use the Arduino UNO board and add more sensor
and module whatever you like.
- to follow the black line on the track from start to finish line. It has
digital line calibration to make it easy.
- to solve the maze courses, you can upload the sketch given or modify
it to remote control via wireless devices (Optional).
- to fight with other opponents robots with in the ring, it has line/
outside avoidance.
- you can add bluetooth, PS2 controller with UHF STD, Ethernet,
Wifi to control it wirelessly.
- Built-in 4-servo slots for EGRA Robotic Arm.
Notes: <number>

## Slide 3: Pbot UNO
SPECIFICATIONS
General Specifications:
Battery: (2)3.7V Li-ion 1000mAh
    rechargeable w/ protection
On-board Peripherals:
- IC Atmega328 w/ 32KB Flash memory
(Original ATMEL IC ATA6614Q)
- IC L9110S Dual Channel PWM Motor Driver
- 2-Ch DC Motor 6V geared 1.5A
- 3-Ch IR line sensor CNY70,10mm range
- 3-Ch IR proximity sensor 2-4inches range
- 1 slot for HC-SR04 Ultrasonic
Distance Sensor
- 1 slot for Wireless module connection
Via Serial Communication (e.g Bluetooth)
PCB Dimensions: 62 mm x 67 mm
* Note: Analog pins A4 and A5 are used to
interface with the system controller, hence
are not available for user shields/application.
Features:
- Efficient Motor Driver circuitry enables
the operation of motor to its maximum power
at the same time eliminating the need for
an heatsink.
- On board 4 ch servo motor driver port
- Sensor managed by independent controller
- Collision sensor are pulsed to saved battery
power.
- Line sensors are digitally calibrated making
calibration process delightfully easy
- Arduino UNO Compatible
- Program it using Arduino IDE 100% code
compatible
- 2-3 hours full charging
- Arduino external I/O pin layout allows you to
plug in any Arduino compatible Shield*
Notes: <number>

## Slide 4: PBOT BOARD reference
MAJOR PARTS
Notes: <number>

## Slide 5: PBOT BOARD actual
Batteries
It has now 2x slot for 3.7V Li-ion battery = 7.4V power supply.
OFF : Parallel batteries 3.7v to charge it.
ON: Series batteries 7.4V
Notes: <number>

## Slide 6: PBOT BOARD actual
Motor Driver L9110s
Modified L9110s 2-Channel Motor Driver with LED indicators.
Notes: <number>

## Slide 7: LINE SENSOR
LINE FOLLOWER CONNECTIONS
LINE SENSORS CONNECTION (P7):
GND,DRV,LN3,LN2,LN1
LINE SENSOR ARRAY:
3 channel Line sensors
LINE CAL – for making line sensor calibrated as easy.
(to calibrate, read the page 9-11)
LINE SENSOR LED INDICATORS:
- LN3(D13), LN2(D12),LN1(D11)
- if LED is ON, black color detected
- if LED is OFF, white color detected
Notes: <number>

## Slide 8: Softwares and library
Arduino IDE Drivers Install this first! Library Add to My Documents>Arduino>libraries
Go to www.arduino.cc >Softwares
Choose your Arduino IDE for your OS.
www.e-gizmo.net/oc/kits documents/ARDUINO IDE SOFTWARES
Download Prolific Driver v10.0 (Windows)
(For Mac OS users) Download md_PL2303_MacOSX
Download eGizmo_Pbot_Uno (Unzip this before you move to libraries)
Notes: <number>

## Slide 9: eGizmo_Pbot_Uno library
Library folder should contains these examples ,src , utility, cpp , h, txt files.
Note: Restart your IDE if you added new libraries in Arduino to recognize it.
Notes: <number>

## Slide 10: Connect the PBOT to PC
USB Connector
USB Cable
Open Arduino IDE.
New Features: Even if your device (PBOT) is OFF you can upload the code.
Connect the USB cable to your laptop and into the device.
Notes: <number>

## Slide 11: Board Select
New Features! PBOT UNO has ATMEGA328P or ARDUINO UNO compatible
Go to Tools> Board>Arduino AVR Boards>Arduino UNO
Notes: <number>

## Slide 12: Select the port
New Features! Serial Port detects if connected while the device is OFF.
Go to Tools> Port> COM #
Troubleshoot
No port? – Install first the Prolific Driver!
Or go to Device Manager> Scan for new devices.
Notes: <number>

## Slide 13: Uploading PBotLine.ino
For line follower
On the Arduino IDE.
1. Line Follower codes
Go to File>Examples>eGizmo_Pbot_Uno>PBotLine
2. Board select
Go to Tools>Boards>Arduino AVR Boards> Arduino UNO
3. Port select
Go to Tools>Port>COM#
Select the correct port
Go to Device Manager
if you're not sure.
Notes: <number>

## Slide 14: LINE SENSOR
CALIBRATION1,2
1. After uploading your code for linesensors.
Turn OFF the POWER switch.
2. Place the eGizmo PBOT controller to the "black
line" then
Turn Off
A.
B.
C.
Turn On
Press and Hold LINE CAL and SYS RST,
while pressing and holding the buttons,
Turn ON the POWER Switch.
LN2 (D12 LED indicator) is ON.
Notes: <number>

## Slide 15: LINE SENSOR
CALIBRATION 3
3. First RELEASE the SYS RST followed by LINE CAL.
Make sure the 3CH Line sensors are faces on the
"black line"
and you will see the LN1 and LN3
(D11 and D13 LED indicators) are
Turn ON and LN1 is blinking.
Now Press LINE CAL once
for the black color calibration.
Notes: <number>

## Slide 16: LINE SENSOR
CALIBRATION 4,5
4. Next, if the L3 (D13 LED indicator) is blinking.
Place the 3CH Line sensors on the "White track".
Then Press LINE CAL again once for the
white color calibration.
After that you will see all the LEDS
for linesensors are ON then it will
turn Off.
5. Now your eGizmo PBOT Controller
Linesensors are calibrated. Then
Press the RESET button or
Switch off and turn ON again.
You can now trace the line and DONE.
Notes: <number>

## Slide 17: LINE FOLLOWER SYNTAX
SYNTAX
PBot.LS1_LEFT();
PBot.LS2_CENTER();
PBot.LS3_RIGHT();
OUTPUT
WHITE LINE DETECTED = 0 or LOW
BLACK LINE DETECTED = 1 or HIGH
EXAMPLES;
If (PBot.LS2_CENTER() == HIGH) // if line sensor 2 center is high
{
Serial.println(“Black line detected!”);
}
LS1
LS2
LS3
Notes: <number>

## Slide 18: MOTORS
CONNECTION SECTION
MOTOR WIRE CONNECTIONS (P2):
MOT 1 – 1A,1B ; MOT2 – 2A,2B
MOT 1 = LEFT
Blue-Bottom
Yellow-Upper
MOT 2 = RIGHT
Green-Upper
Black-Bottom
*Please don not depends on the color of the wires.
Follow the location of it.
Notes: <number>

## Slide 19: Uploading PBotMotorTest.ino
Direction/Speed
On the Arduino IDE.
1. Motor controls codes
Go to File>Examples>eGizmo_Pbot_UNO>PbotMotorTest
Notes: <number>

## Slide 20: MOTOR CONTROLS SYNTAX
SYNTAX
Set motor direction:
PBot.DIRECTION(whichmotor,dir);
where:
whichmotor = MOTOR_A or MOTOR_B, MOTOR_BOTH
dir = MOTOR_FWD,MOTOR_REV
EXAMPLES;
PBot.DIRECTION(MOTOR_BOTH, MOTOR_FWD); // Move Forward
PBot.SPEED(MOTOR_BOTH, 80);
Set motor speed:
PBot.SPEED(whichmotor,speed);
where:
whichmotor = MOTOR_A or MOTOR_B, MOTOR_BOTH
speed = 0 to 255, 0 = Full Stop, 80 = Neutral,255 = High, limit 250
Notes: <number>

## Slide 21: MAZE/SUMO
IR SENSORS CONNECTIONS
IR RECEIVERS 38Khz
- U5, U6, U7
IR LED TRASMITTER
- D17, D18, D19
- Distance Range: 2 – 4 inches
IR LED INDICATORS
- COL1 (D14), COL2 (D15), COL3 (D16)
- if LED is ON, Object detected
- if LED is OFF, No object detected
Notes: <number>

## Slide 22: Uploading PBotSumo.ino
Sumo Fight
On the Arduino IDE.
1. Sumo fighting codes
Go to File>Examples>eGizmo_PBot_Uno>PBotSumo
Notes: <number>

## Slide 23: IR SENSORS SYNTAX
SYNTAX
PBot.COL1_RIGHT();
PBot.COL2_CENTER();
PBot.COL3_LEFT();
OUTPUT
NO OBJECT DETECTED = 0 or LOW
OBJECT DETECTED = 1 or HIGH
EXAMPLES;
If (PBot.COL2_CENTER() == HIGH) // if IR sensor 2 center is high
{
Serial.println(“Object detected!”);
}
!
Notes: <number>

## Slide 24: SERVO MOTOR
CONNECTION
Servo labels #1-#4
Servo connectors from
P3 - P6
Notes: <number>

## Slide 25: Uploading PBotServo.ino
Servo Controls
On the Arduino IDE.
1. Servo codes
Go to File>Examples>eGizmo_Pbot_Uno>PBotServo
Notes: <number>

## Slide 26: SERVO SYNTAX
SYNTAX
Pbot.SERVO(whichSERVO,pulsewidth);
where:
Whichservo = 1 to 4, ignore other values
Pulsewidth = 0 to 180 (degrees)
- value less than 500 stops the Servo PWM generator
- the pulsewidth converted to degrees from 0 to 180 (default)
EXAMPLES;
PBot.SERVO(1, 15);
delay(1000);
PBot.SERVo(1, 90);
delay(1000);
Notes: <number>

## Slide 27: Arduino Shield
Accessible Pins
IO0 to IO17 (18 Digital Pins)
A0-A3 (4 Analog Input pins)
* A4 and A5 are used
Where you can add Bluetooth Shield or other
Interface shields.
Notes: <number>

## Slide 28: Distance sensor pin slot - Hardware Serial pin slot
Additional Features on board
Notes: <number>

## Slide 29: DISTANCE SENSOR
CONNECTION
J1 -- reference
GND -- Ground
ECH -- Echo
TRI -- Trigger
+5V -- Vcc
Distance Sensor Slot
Notes: <number>

## Slide 30: Uploading PBotDistanceSensor.ino
Distance Sensor
On the Arduino IDE.
1. Distance sensor codes
Go to File>Examples>eGizmo_Pbot_Uno>PBotDistanceSensor
Notes: <number>

## Slide 31: DISTANCE SYNTAX
SYNTAX
Pbot.DISTANCE();
Where:
Reading the distance sensor
Pbot.RANGE;
Where:
Getting the data in Centimeter/cm
EXAMPLES;
Pbot.DISTANCE();
Serial.print(“Measure in cm = “);
Serial.println(PBot.RANGE);
delay(10);
Notes: <number>

## Slide 32: BT CONTROLLED via Serial
CONNECTION
WIRELESS – Reference
RXD -- Received
TXD -- Transmitted
GND -- Ground
+5V –- Vcc
Notes: <number>

## Slide 33: Uploading PBotBTControlled.ino
Wireless Connection
On the Arduino IDE.
1. Bluetooth Control codes
Go to File>Examples>eGizmo_Pbot_Uno>PBotBTControlled
Notes: <number>

## Slide 34: BLUETOOTH SYNTAX
SYNTAX
Byte INPUT_FROM_ANDROID_APP;
//Main Program
If(Serial.available() > 0){
INPUT_FROM_ANDROID_APP = Serial.read();
Serial.println(INPUT_FROM_ANDROID_APP);
}
EXAMPLES;
If (INPUT_FROM_ANDROID_APP == 11) { } //UP BUTTON
If (INPUT_FROM_ANDROID_APP == 12) { } //DOWN BUTTON
If (INPUT_FROM_ANDROID_APP == 13) { } //LEFT BUTTON
If (INPUT_FROM_ANDROID_APP == 14) { } //RIGHT BUTTON
If (INPUT_FROM_ANDROID_APP == 0) { } //STOP BUTTON
If (INPUT_FROM_ANDROID_APP == 17) { } //KICK BUTTON
If (INPUT_FROM_ANDROID_APP == 18) { }
If (INPUT_FROM_ANDROID_APP == 15) { }
If (INPUT_FROM_ANDROID_APP == 16) { }
Notes: <number>

## Slide 35
Website: https://www.e-gizmo.net
Egizmo Tech blog: https://www.e-gizmo.net/oc/index.php?route=journal3/blog
Facebook: https://www.facebook.com/eGizmoMechatronix
Youtube Channel: e-Gizmo Mechatronix Central
For more info.
Notes: <number>